## Slide 1: Address Spaces, Base + Limit Registers, and Contiguous Allocation
David Ferry CSCI 3500 – Operating Systems
Saint Louis University St. Louis, MO 63103

## Slide 2: Recall: Real Mode Memory
Addresses seen at the processor are the physical addresses in hardware:
No isolation between processes
No isolation between OS and userspace
Limited multi-tasking (swapping and partitioning)
Relocation is difficult
OS
Program 1
OS
Program 2
Load Program 1
Save Program 1 Load Program 2
OS
Program 1
Program 2
Program 3

## Slide 3: Virtual Memory: Virtual Address Spaces
0x0
0xFFFF…
Kernel Space
User Space
Operating System
Program
Program
Program
Library
Physical Memory (RAM)
.heap
.stack
.text
.data
Virtual Address Space
0x0
0xFFFF…
Programs see and use virtual memory addresses at the CPU
Addresses must be translated between virtual and physical by hardware called the Memory Management Unit (MMU)
Translation must be fast- doing everything in software would be too slow- need HW acceleration
.heap
.stack
.text
.data
Virtual Address Space
0x0
0xFFFF…

## Slide 4: Implementing Address Spaces with Base + Limit Registers
Two special CPU registers keep track of each process’ start (base) and size (limit)
Registers are only modifiable by the OS
Data becomes part of process context and is swapped in context switches
All memory accesses are checked against base and limit
Out-of-range accesses are errors (e.g. segfault)
0x0
Operating System
Program
Program
Program
0xFFFF…
Base = 0x1000
Limit = 0x2000

## Slide 5: Base + Limit Advantages (over Real Mode)
Each process has an independent virtual address space
Implements process isolation
  Programs cannot maliciously or accidentally interfere with each other or the OS
Relocation is now easy
  Add the base register to every address leaving the CPU
  No need to modify programs when loaded
Put many programs in memory
Operating System
Program
Program
Program
0xFFFF…
Base
Limit
Base
Limit
Base
Limit

## Slide 6: Base + Limit Relocation Example
.heap
.stack
.text
.data
Virtual Address Space
0x0
0xFFFF…
Base Register: 0x2000
Virtual Address: 0x0123
ADD
Physical Address:
0x2123
Operating System
Program
Program
Program
Library

## Slide 7: Base + Limit Isolation Example
Suppose Base = 0x2000 and Limit = 0x3000
Base Register: 0x2000
Virtual Address: -0x0200
ADD
Physical Address:
0x1E00
<
Base Register: 0x2000
ERROR

## Slide 8: Base + Limit Isolation Example
Suppose Base = 0x2000 and Limit = 0x3000
Base Register: 0x2000
Virtual Address: 0x1500
ADD
Physical Address:
0x3500
<
Base Register: 0x2000
ERROR
>
Limit Register: 0x3000
Physical Address:
0x3500

## Slide 9: Where do we allocate programs?
We now have a mechanism for loading many programs dynamically
In real mode we usually only had one program, or at most a few programs that were carefully managed by hand
We don’t want the user to have to manually manage where to put programs in memory
Can the machine allocate memory space for us?
One fundamental limitation: Programs must be contiguous

## Slide 10: Contiguous Allocation: Fragmentation
Base + Limit scheme requires programs to be contiguous (continuous, with no gaps) in memory
Operating System
Program A 0x1500
0x0
0x4000
0x3000
Operating System
Program B 0x500
Program A 0x1500
Operating System
Program B 0x500
Operating System
Program B 0x500
Program C 0x500
At the end of the sequence we have 0x2000 bytes free but only 0x1000 bytes of contiguous memory
The memory space is fragmented
Compaction could move programs around, but this is slow and causes interference

## Slide 11: Placement Algorithms
No single best approach to placing programs in memory:
Minimize fragmentation?
Keep big chunks available?
Optimize for speed?
We can view memory placement as a type of bin packing algorithm with heuristics corresponding to the above concerns:
Best Fit
Worst Fit
First Fit