## Slide 1: Page Tables and the Translation Lookaside Buffer (TLB)
David Ferry CSCI 3500 – Operating Systems
Saint Louis University St. Louis, MO 63103

## Slide 2: Recall: Paging
Paging
Divide a program’s virtual memory into pages
Divide physical memory into page frames
Pages are taken from the hard drive and placed in memory as needed
Programs do not need to be contiguous in memory, don’t even need to be in order
Programs can be partially in memory
Program 1
A
B
C
D
Program 2
A
B
C
D
…
…
Memory
…
A
B
A
C
D
B

## Slide 3: Recall: Paging Address Translation
Suppose 4KB pages and page 1 is mapped into memory at page frame 5
Page Start: 4096
Virtual Address: 7000
SUB
Page Offset:
2904
ADD
Page Frame Start: 20,480
Physical Address:
23,384
This is a very math-heavy translation method- it describes what is happening in principle, but would be too slow in a real system

## Slide 4: Page Tables
The data structure that stores the mapping between pages and page frames, plus stores page metadata
Enables easier translation than math-heavy approach
Page Table is a per-process data structure in the OS
A modern page table:
Page Num | Frame Num | Present | Referenced | Modified | Protection
0000 | 00111 | 1 | 1 | 0 | R - X
0001 | 00010 | 1 | 1 | 1 | R W -
0010 | 01001 | 0 | 0 | 0 | R W -
0011 | 01101 | 1 | 1 | 0 | R - -
…
…
…
…
…
…

## Slide 5: Page Table Elements
Page Number – The page number in the virtual address space, table is arranged sequentially by page number
Frame Number – The page frame number in physical memory that the virtual page resides in
Present – Is the page currently in memory or not? Is the mapping in the page table valid?
Referenced – Is the page currently being used by the process?
Modified – Is the page in physical memory different than what is currently stored in long-term storage?
Permissions – Read/Write/Execute permissions for a page. For example, program code is usually R/X, program data is usually R/W, but constant or read-only data is just R

## Slide 6: Page Table Translation
0001010011100101
Page Frame Number: 11010
Page Number: 0001
Offset: 010011100101
Suppose we have a 16-bit virtual address & 4KB pages.
Translate the following virtual address to its physical address:
Page Num | Frame Num | Present | Referenced | Modified | Protection
0000 | 00111 | 1 | 1 | 0 | R - X
0001 | 11010 | 1 | 1 | 1 | R W -
0010 | 01001 | 0 | 0 | 0 | R W -
0011 | 01101 | 1 | 1 | 0 | R - -
…
…
…
…
…
…
Offset: 010011100101
Physical Address: 11010010011100101

## Slide 7: Page Table Translation: Notes
Virtual Address: 0001010011100101
Page Number: 0001
Offset: 010011100101
Page Frame Number: 11010
Offset: 010011100101
Physical Address: 11010010011100101
Notes:
The leading bits of the virtual address are naturally the page number! This is because pages are ordered sequentially in virtual memory.
The offset (in binary) is exactly what we would have calculated if we did the translation the long-hand way.
The page size is 212 bytes, and there are 12 bits in the offset! This is not a coincidence. The offset describes which byte an address references within a page, which does not change under translation.
The page frame number can be longer, the page number can be longer, or they can be equal. What determines the length of each?
The offset will always stay the same length (and the same value) between virtual and physical.

## Slide 8: Page Table Performance
Paging with page tables is flexible, but suffers from two performance problems:
Page table can become very large: Suppose we have 32-bit addresses with 4KB pages- how many pages? It’s 232 / 212 = 220 pages = approx. 1 million How big is one row in the page table? For 32-bits above then the page number is 20 bits. The frame number will be similar. Plus metadata, let’s round up to six bytes per row. 1 million rows @ 6 bytes per row => 6 MB Remember this is a per-process data structure

## Slide 9: Page Table Performance 2
We can do the same thought experiment with 64-bit architectures (48-bit virtual addresses)
Page table can become very large: Suppose we have 48-bit addresses with 4KB pages- how many pages? It’s 248 / 212 = 236 pages = approx. 64 billion How big is one row in the page table? For 48-bits above then the page number is 36 bits. The frame number will be similar. Plus metadata, let’s round up to 10 bytes per row. 64 billion rows @ 10 bytes per row => 640 GB Remember this is a per-process data structure

## Slide 10: Page Table Performance 3
The second performance problem:
Translation must be fast
  Recall that ~10% of instructions are memory references
  If the page table is stored in memory, then for every memory reference we need to go back to memory a second time just to figure out the page mapping
  Even worse, consider that some high level languages have single instructions that can generate two or three memory references

## Slide 11: Hardware Accelerated Page Tables
We want the flexibility of paging, but also the speed of hardware. Solution: the translation lookaside-buffer (TLB)
Observation: Most programs only use a few pages at a time
A small hardware cache of frequently used pages and their frame mapping would accelerate most programs effectively
Can use associative memory to speed things up even more
Valid | Page Num | Modified | Protection | Frame Num
1 | 0001 | 0 | R - X | 00111
1 | 0110 | 1 | R W - | 00010
0 | 0010 | 0 | R W - | 01001
1 | 0101 | 0 | R - - | 01101
Query: 0110
Result: 00010

## Slide 12: Modern Memory Architecture
Hit Physical Address
CPU
Memory Management Unit (MMU)
TLB
Physical Memory (RAM)
Page Table
Desired Page Frame
Virtual Address
Returned Data
Miss
Page Mapping
Disk
Not Present Page Frames
CPU generates virtual address
If the page mapping is available in TLB; HIT, go directly to physical address
  If page mapping not available in TLB; MISS, go to page table to get mapping (also called a minor or soft page fault)
If the page is not currently loaded in memory, load it from disk (major or hard page fault)

## Slide 13: Notes on Performance
A modern TLB can “hit” in a cycle or less, meaning that memory addresses are translated with no slowdown on a hot cache
Access to main memory can take 100+ cycles on modern architectures, so a TLB soft page fault can have a penalty of 100 cycles or more
TLB accuracy is generally very high- 60% to 99.99% depending on application
Q: Suppose a TLB is 99% accurate, takes 1 cycle when it hits, and has a miss penalty of 100 cycles. What is the average time it takes to resolve a physical address?
A: (1 cycle)*.99 + (100 cycles)*0.01 = 1.99 cycles