## Slide 1: Computer Networking
David Ferry CSCI 3500 – Operating Systems
Saint Louis University St. Louis, MO 63103

## Slide 2: How are Networks connected to the OS?
Most users don’t want to implement their own network code, they want it available as a service. Where should that service be handled?
Networking necessarily has multiple processes interacting
  Those processes could be on the same machine, or different machines
The OS has to be involved- but to what degree?
  We can implement networking entirely in the OS
  We could use userspace library but still need significant OS support
The OS implements networking in most modern Oses
As a curriculum issue:
OS is last required systems course
Very much a systems topic

## Slide 3: Theory of Networking
Computer networks are some of the most complex artifacts we’ve ever built:
Greater than 1 billion hosts
Spans every country on Earth, plus space
Numerous hardware and software providers
Key idea to manage complexity: Layered abstraction
Divide the tasks required to support computer communication into multiple levels
Each level communicates with the layer above & below it in a well-defined manner
Creates a set of small, manageable pieces to work with

## Slide 4: Layered Abstraction
OSI 7-Layer Model:
I.e. “the network stack”
Each layer has a logical connection to its corresponding layers on remote machines
Strict separation is a general rule, but there are some cross-cutting concerns (security, reliability, etc.)
Application
Presentation
Session
Transport
Network
Data-Link
Physical
Application
Presentation
Session
Transport
Network
Data-Link
Physical
Process to Process
Hardware to Hardware
Interface to Interface
Physical Connection
Application to Application
Entity to Entity
Protocol to Protocol
Userspace
Kernel Space

## Slide 5: Data Flow
Application
Data
Transport
Data
TCP Header
Network
Data
TCP Header
IP Header
Data Link
Data
TCP Header
IP Header
Frame
Frame
Data originates at the application layer, and each layer permutes the data in turn. When it is received those changes are undone in reverse.

## Slide 6: What’s next?
We will look at each layer in the OSI model in more detail
  Some layers we’ll have more to say than others…
We will look at the sockets software interface used to implement networked programs
Lab 5 and our last studios will have you implement your own networked programs
  A lot easier than you might think!