## Slide 1: Physical and Data-Link Layers
David Ferry CSCI 3500 – Operating Systems
Saint Louis University St. Louis, MO 63103

## Slide 2: Recall: Layered Abstraction
Each layer has a logical connection to its corresponding layer
Data originates at the application layer and makes it’s way up and down the stack as necessary
Application
Presentation
Session
Transport
Network
Data-Link
Physical
Application
Presentation
Session
Transport
Network
Data-Link
Physical
Process to Process
Hardware to Hardware
Interface to Interface
Physical Connection
Application to Application
Entity to Entity
Protocol to Protocol
Userspace
Kernel Space

## Slide 3: Physical Layer
Specifies the physical communication medium, such as:
Wire size, twists per inch
Connectors
Voltages
Radio frequencies
Timings
Representation of a bit
Example: 10BASE-T stands for a 10 Megabit baseband transmission over twisted pair wiring
8-pin ethernet cable
+/- 2.5-volt signaling

## Slide 4: Data-Link Layer
Uses the physical layer to communicate between devices
Examples: Ethernet, 802.11 Wi-Fi, GSM voice/data
Each device is a distinct communication endpoint identified via MAC addresses:
MAC (Media Access Control) Address:
Identifies a device that can send/receive over the medium
Some media can have many devices: e.g. Wi-Fi or Ethernet when using a hub
6 bytes- e.g. 1A:2B:3C:4D:5E:6F
This ID is only used for signaling, any device can change its MAC address whenever it wants

## Slide 5: Data-Link Frames
Data-Link question: How do I send a frame of data from one device to another?
Ethernet Frame:
Preamble: 56 alternating 1’s and 0’s
Frame start: unique start byte
Ethertype: specifies type of payload
CRC: ensures data integrity
Preamble | Frame Start | MAC Destination | MAC Source | Ethertype | Payload | CRC
7 bytes | 1 byte | 6 bytes | 6 bytes | 2 bytes | Up to 1500 bytes | 4 bytes

## Slide 6: Ethernet Transmission Protocol
Frames are sent under the Carrier Sense – Multiple Access with Collision Detection protocol, or CSMA/CD for short
Ready frame for transmission
Wait for an idle medium
Transmit and monitor for collision
If collision:
  Send jamming signal
  If exceeds max_retries then abort
  Otherwise retransmit with random exponential backoff

## Slide 7: Exponential Backoff
Problem: When do we try and retransmit after a collision?
Can’t retry immediately- why?
Adding a random delay helps reduce number of repeat collisions for a small number of devices.
What if a channel is very busy and many collisions could occur? Exponential backoff clears the congestion rapidly. E.g.:
First collision wait 10-20us
Second collision wait 20-100us
Third collision wait 100-1000us, etc.

## Slide 8: Ensuring Data Integrity
Problem: How to ensure that the message received is the message that was intended to be sent?
The electronic world is a noisy place- bit flips, etc. regularly happen.
Easiest possible algorithm: transmit the same message two, three, or more times and compare for accuracy
  Why not use this?
The CRC is a hash function:
The hash is not stable- flipping even one bit of an input leads to a different hash outcome
The hash is fast to compute in hardware, unlike our cryptographic hashes we used earlier in the course

## Slide 9: CRC Procedure
After the frame has been readied, the sender computes the CRC check value appends it to the frame
The frame is transmitted
After the frame is received, the receiver re-computes the CRC check value
If the two values match, then the frame is very highly likely to be intact (small chance of hash collisions)
If they do not match, the frame is discarded

## Slide 10: What next?
We have seen how two machines directly connected via the same medium can exchange messages.
What if they’re not on the same medium? E.g. what if A and C want to talk via a shared friend called B?
Application
Presentation
Session
Transport
Network
Data-Link
Physical
Application
Presentation
Session
Transport
Network
Data-Link
Physical
Process to Process
Hardware to Hardware
Interface to Interface
Physical Connection
Application to Application
Entity to Entity
Protocol to Protocol