## Slide 1
Randal E. Bryant
adapted by Jason Fritts
CS:APP2e
CS:APP Chapter 4
Computer Architecture
Pipelined
Implementation
http://csapp.cs.cmu.edu

## Slide 2: Overview
General Principles of Pipelining
  Goal
  Difficulties
Creating a Pipelined Y86 Processor
  Rearranging SEQ to create pipelined datapath, PIPE
  Inserting pipeline registers
  Problems with data and control hazards

## Slide 3: Fundamentals of Pipelining

## Slide 4: Real-World Pipelines: Car Washes
Idea
  Divide process into independent stages
  Move objects through stages in sequence
  At any given times, multiple objects being processed
Sequential
Parallel
Pipelined

## Slide 5: Computational Example
System
  Computation requires total of 300 picoseconds
  Additional 20 picoseconds to save result in register
  Must have clock cycle of at least 320 ps
Combinational
logic
R
e
g
300 ps
20 ps
Clock
Delay = 320 ps
Throughput = 3.12 GIPS

## Slide 6: 3-Way Pipelined Version
System
  Divide combinational logic into 3 blocks of 100 ps each
  Can begin new operation as soon as previous one passes through stage A.
    Begin new operation every 120 ps
  Overall latency increases
    360 ps from start to finish
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Delay = 360 ps
Throughput = 8.33 GIPS

## Slide 7: Pipeline Diagrams
Unpipelined
  Cannot start new operation until previous one completes
3-Way Pipelined
  Up to 3 operations in process simultaneously
Time
OP1
OP2
OP3
Time
A
B
C
A
B
C
A
B
C
OP1
OP2
OP3

## Slide 8: Operating a Pipeline
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C
0
120
240
360
480
640
Clock
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
239
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
241
R
e
g
R
e
g
R
e
g
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Comb.
logic
A
Comb.
logic
B
Comb.
logic
C
Clock
300
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
359

## Slide 9: Limitations: Nonuniform Delays
  Throughput limited by slowest stage
  Other stages sit idle for much of the time
  Challenging to partition system into balanced stages
R
e
g
Clock
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
50 ps
20 ps
150 ps
20 ps
100 ps
20 ps
Delay = 510 ps
Throughput = 5.88 GIPS
Comb.
logic
A
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C

## Slide 10: Sample Circuit Delays & Pipelining
Single-cycle processor:
  Clock cycle = 220 + 70 + 120 + 180 + 260 + 120 + 20 = 990ps
  Clock freq = 1 / 990ps = 1 / 990*10-12 = 1.01 GHz
Combine and/or split stages for pipelining
  Need to balance time per stage since clock freq determined by slowest time
  Must maintain original order of stages, so can’t combine non-neighboring stages (e.g. can’t combine decode & data mem)
20ps delay for hardware register at end of cycle

## Slide 11: Sample Circuit Delays & Pipelining
3-stage pipeline:
  Best combination for minimizing clock cycle time:
    1st stage – instr mem & decode: 220 + 70 + 20 = 310ps
    2nd stage – reg fetch & ALU: 120 + 180 + 20 = 320ps
    3rd stage – data mem & reg WB: 260 + 120 + 20 = 400ps
  Slowest stage is 400ps, so clock cycle time is 400ps
  Clock freq = 1 / 400ps = 1 / 400*10-12 = 2.5 GHz
20ps delay added for hardware register at end of each cycle

## Slide 12: Sample Circuit Delays & Pipelining
5-stage pipeline:
  Best combination for minimizing clock cycle time:
    1st stage – instr mem: 220 + 20ps = 240ps
    2nd stage – decode & reg fetch: 70 + 120 + 20ps = 210ps
    3rd stage – ALU: 180 + 20ps = 200ps
    4th stage – data mem: 260 + 20ps = 280ps
    5th stage – reg WB: 120 + 20ps = 140ps
  Slowest stage is 400ps, so clock cycle time is 280ps
  Clock freq = 1 / 280ps = 1 / 280*10-12 = 3.57 GHz
20ps delay added for hardware register at end of each cycle

## Slide 13: Sample Circuit Delays & Pipelining
9-stage pipeline:
  Assuming can split stages evenly into halves, thirds, or quarters
    not a valid assumption, but useful for simplifying problem
  Best combination for minimizing clock cycle time:
    Each circuit is its own stage, with 20ps added delay for reg
    Split instr mem circuit into two stages, each 110+20ps
    Split data mem circuit into two stages, each 130+20ps
    Split ALU circuit into two stages, each 90+20ps
  Slowest stage is 150ps, so clock cycle time is 150ps
  Clock freq = 1 / 150ps = 1 / 150*10-12 = 6.67 GHz
20ps delay added for hardware register at end of each cycle

## Slide 14: Limitations: Register Overhead
  As try to deepen pipeline, overhead of loading registers becomes more significant
  Percentage of clock cycle spent loading register:
    1-stage pipeline: 6.25%
    3-stage pipeline: 16.67%
    6-stage pipeline: 28.57%
  High speeds of modern processor designs obtained through very deep pipelining
Delay = 420 ps, Throughput = 14.29 GIPS
Clock
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps

## Slide 15: Converting SEQ to PIPE, a pipelined datapath

## Slide 16: SEQ Hardware
  Stages occur in sequence
  One operation in process at a time
To convert to pipelined datapath, start by adding registers between stages, resulting in 5 pipeline stages:
  Fetch
  Decode
  Execute
  Memory
  Writeback

## Slide 17: Converting to pipelined datapath
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC
Add pipeline registers between stages

## Slide 18: Problem: Fetching a new instruction each cycle
Two problems
  PC generated in last stage of SEQ datapath
  PC sometimes not available until end of Execute or Memory stage
PC needs to be computed early
  In order to fetch a new instruction every cycle, PC generation must be moved to first stage of datapath
  Solve first problem by moving PC generation from end of SEQ to beginning of SEQ
Use prediction to select PC early
  Solve second problem by predicting next instruction from current instruction
  If prediction is wrong, squash (kill) predicted instructions

## Slide 19: SEQ+ Hardware
  Still sequential implementation
  Reorder PC stage to put at beginning
PC Stage
  Task is to select PC for current instruction
  Based on results computed by previous instruction
Processor State
  PC is no longer stored in register
  But, can determine PC based on other stored information

## Slide 20: Predicting the PC
  Start fetch of new instruction after current has been fetched
    Not enough time to fully determine next instruction
  Attempt to predict which instruction will be next
    Recover if prediction was incorrect

## Slide 21: Our Prediction Strategy
  Predict next instruction from current instruction
Instructions that Don’t Transfer Control
  Predict next PC to be valP
  Always reliable
Call and Unconditional Jumps
  Predict next PC to be valC (destination)
  Always reliable
Conditional Jumps
  Predict next PC to be valC (destination)
  Only correct if branch is taken
    Typically right 60% of time
Return Instruction
  Don’t predict, just stall

## Slide 22: Recovering from PC Misprediction
Mispredicted Jump
  Will see branch condition flag once instruction reaches memory stage
  Can get fall-through PC from valA (value M_valA)
Return Instruction
  Will get return PC when ret reaches write-back stage (W_valM)

## Slide 23: Pipeline Stages
Fetch
  Select current PC
  Read instruction
  Compute incremented PC
Decode
  Read program registers
Execute
  Operate ALU
Memory
  Read or write data memory
Write Back
  Update register file

## Slide 24: PIPE- Hardware
  Pipeline registers hold intermediate values from instruction execution
Forward (Upward) Paths
  Values passed from one stage to next
  Cannot jump past stages
    e.g., valC passes through decode

## Slide 25: Feedback Paths
Important for distinguishing dependencies between pipeline stages
Predicted PC
  Guess value of next PC
Branch information
  Jump taken/not-taken
  Fall-through or target address
Return point
  Read from memory
Register updates
  To register file write ports

## Slide 26: Signal Naming Conventions
S_Field
  Value of Field held in stage S pipeline register
s_Field
  Value of Field computed in stage S

## Slide 27: Dealing with Dependencies between Instructions

## Slide 28: Hazards
Hazards
  Problems caused by dependencies between separate instructions in the pipeline
Data Hazards
  Instruction having register R as source follows shortly after instruction having register R as destination
  Common condition, don’t want to slow down pipeline
Control Hazards
  Mispredict conditional branch
    Our design predicts all branches as being taken
    Naïve pipeline executes two extra instructions
  Getting return address for ret instruction
    Naïve pipeline executes three extra instructions

## Slide 29: Dealing with Dependencies between Instructions
Data Hazards

## Slide 30: Data Dependencies - not a problem in SEQ
System
  Each operation depends on result from preceding one
Clock
Combinational
logic
R
e
g
Time
OP1
OP2
OP3

## Slide 31: Data Hazards - the problems caused by data dependences in pipelined datapaths
  Result does not feed back around in time for next operation
  Pipelining has changed behavior of system
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C
OP4
A
B
C

## Slide 32: Data Dependencies between Instructions
  Result from one instruction used as operand for another
    Read-after-write (RAW) dependency
  Very common in actual programs
  Must make sure our pipeline handles these properly
    Get correct results
    Minimize performance impact
1 irmovl $50, %eax
2 addl %eax , %ebx
3 mrmovl 100( %ebx ), %edx

## Slide 33: Data Dependencies – Loop-Carried Dependencies
rmmovl %edi, 0(%edx)
LOOP: mrmovl 0(%ecx), %edi
mrmovl 12(%esp),%ebx
mrmovl 8(%esp), %edx
mrmovl 4(%esp), %ecx
mrmovl 0(%edx), %eax
addl %eax, %edi
iaddl $4, %ecx
iaddl $4, %edx
iaddl $-1, %ebx
jne LOOP
%ecx
%edx
%edx
%ecx
%edx
%ebx

## Slide 34: Pipeline Demonstration
File: demo-basic.ys
irmovl $1,%eax #I1
1
2
3
4
5
6
7
8
9
F
D
E
M
W
irmovl $2,%ecx #I2
F
D
E
M
W
irmovl $3,%edx #I3
F
D
E
M
W
irmovl $4,%ebx #I4
F
D
E
M
W
halt #I5
F
D
E
M
W
Cycle 5
W
I1
M
I2
E
I3
D
I4
F
I5
All the instructions are independent
of each other
- No dependencies exist

## Slide 35: Data Dependencies: 3 Nop’s
0x000:
irmovl
$10,%
edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x006:
irmovl
$3,%
eax
F
D
E
M
W
F
D
E
M
W
0x00c:
nop
F
D
E
M
W
F
D
E
M
W
0x00d:
nop
F
D
E
M
W
F
D
E
M
W
0x00e:
nop
F
D
E
M
W
F
D
E
M
W
0x00f:
addl
%
edx
,%
eax
F
D
E
M
W
F
D
E
M
W
10
W
R[
%
eax
]
f
3
W
R[
%
eax
]
f
3
D
valA
f
R[
%
edx
]
=
10
valB
f
R[
%
eax
]
=
3
D
valA
f
R[
%
edx
]
=
10
valB
f
R[
%
eax
]
=
3
# demo-h3.ys
Cycle 6
11
0x011: halt
F
D
E
M
W
F
D
E
M
W
Cycle 7
The addl instruction depends on the first two instructions
addl depends upon %edx from the 1st instr
addl depends upon %eax from the 2nd instr
addl must wait 3 cycles after the 2nd instruction, so that it doesn’t fetch the two registers before they’ve been written to the register file

## Slide 36: Data Dependencies: 2 Nop’s
0x000:
irmovl
$10,%
edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x006:
irmovl
$3,%
eax
F
D
E
M
W
F
D
E
M
W
0x00c:
nop
F
D
E
M
W
F
D
E
M
W
0x00d:
nop
F
D
E
M
W
F
D
E
M
W
0x00e:
addl
%
edx
,%
eax
F
D
E
M
W
F
D
E
M
W
0x010: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-h2.ys
W
R[
%
eax
]
f
3
D
valA
f
R[
%
edx
]
=
10
valB
f
R[
%
eax
]
=
0
•
•
•
W
R[
%
eax
]
f
3
W
R[
%
eax
]
f
3
D
valA
f
R[
%
edx
]
=
10
valB
f
R[
%
eax
]
=
0
D
valA
f
R[
%
edx
]
=
10
valB
f
R[
%
eax
]
=
0
•
•
•
Cycle 6
Error
If addl executes one cycle earlier, it gets the wrong value for %eax

## Slide 37: Data Dependencies: 1 Nop
0x000:
irmovl
$10,%
edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x006:
irmovl
$3,%
eax
F
D
E
M
W
0x00c:
nop
F
D
E
M
W
F
D
E
M
W
0x00d:
addl
%
edx
,%
eax
F
D
E
M
W
F
D
E
M
W
0x00f: halt
F
D
E
M
W
F
D
E
M
W
# demo-h1.ys
W
R[
%
edx
]
f
10
W
R[
%
edx
]
f
10
D
valA
f
R[
%
edx
]
=
0
valB
f
R[
%
eax
]
=
0
D
valA
f
R[
%
edx
]
=
0
valB
f
R[
%
eax
]
=
0
•
•
•
Cycle 5
Error
M
M_
valE
= 3
M_
dstE
=
%
eax
If addl executes two cycles earlier, it gets the wrong value for both %eax and %ebx

## Slide 38: Data Dependencies: No Nop
0x000:
irmovl
$10,%
edx
1
2
3
4
5
6
7
8
F
D
E
M
W
0x006:
irmovl
$3,%
eax
F
D
E
M
W
F
D
E
M
W
0x00c:
addl
%
edx
,%
eax
F
D
E
M
W
0x00e: halt
# demo-h0.ys
E
D
valA
f
R[
%
edx
]
=
0
valB
f
R[
%
eax
]
=
0
D
valA
f
R[
%
edx
]
=
0
valB
f
R[
%
eax
]
=
0
Cycle 4
Error
M
M_
valE
= 10
M_
dstE
=
%
edx
e_
valE
f
0 + 3 = 3
E_
dstE
=
%
eax
Like the prior case, if addl executes three cycles earlier, it gets the wrong value for both %eax and %ebx

## Slide 39: Stalling for Data Dependencies
  If instruction follows too closely after one that writes register, slow it down
  Hold instruction in decode
  Dynamically inject nop into execute stage
0x000: irmovl $10,%edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x006: irmovl $3,%eax
F
D
E
M
W
0x00c: nop
F
D
E
M
W
bubble
F
E
M
W
0x00e: addl %edx,%eax
D
D
E
M
W
0x010: halt
F
D
E
M
W
10
# demo-h2.ys
F
F
D
E
M
W
0x00d: nop
11

## Slide 40: Stall Condition
Source Registers
  srcA and srcB of current instruction in decode stage
Destination Registers
  dstE and dstM fields
  Instructions in execute, memory, and write-back stages
Special Case
  Don’t stall for register ID 15 (0xF)
    Indicates absence of register operand
  Don’t stall for failed conditional move

## Slide 41: Detecting Stall Condition
0x000: irmovl $10,%edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x006: irmovl $3,%eax
F
D
E
M
W
0x00c: nop
F
D
E
M
W
bubble
F
E
M
W
0x00e: addl %edx,%eax
D
D
E
M
W
0x010: halt
F
D
E
M
W
10
# demo-h2.ys
F
F
D
E
M
W
0x00d: nop
11
Cycle 6
W
D
•
•
•
W_dstE = %eax
W_valE = 3
srcA = %edx
srcB = %eax

## Slide 42: Stalling X3
0x000: irmovl $10,%edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x006: irmovl $3,%eax
F
D
E
M
W
bubble
F
E
M
W
bubble
D
E
M
W
0x00c: addl %edx,%eax
D
D
E
M
W
0x00e: halt
F
D
E
M
W
10
# demo-h0.ys
F
F
D
F
E
M
W
bubble
11
Cycle 4
•
•
•
W
W_dstE = %eax
D
srcA = %edx
srcB = %eax
•
•
•
M
M_dstE = %eax
D
srcA = %edx
srcB = %eax
E
E_dstE = %eax
D
srcA = %edx
srcB = %eax
Cycle 5
Cycle 6

## Slide 43: What Happens When Stalling?
  Stalling instruction held back in decode stage
  Following instruction stays in fetch stage
  Bubbles injected into execute stage
    Like dynamically generated nop’s
    Move through later stages
0x000: irmovl $10,%edx
0x006: irmovl $3,%eax
0x00c: addl %edx,%eax
Cycle 4
0x00e: halt
0x000: irmovl $10,%edx
0x006: irmovl $3,%eax
0x00c: addl %edx,%eax
# demo-h0.ys
0x00e: halt
0x000: irmovl $10,%edx
0x006: irmovl $3,%eax
bubble
0x00c: addl %edx,%eax
Cycle 5
0x00e: halt
0x006: irmovl $3,%eax
bubble
0x00c: addl %edx,%eax
bubble
Cycle 6
0x00e: halt
bubble
bubble
0x00c: addl %edx,%eax
bubble
Cycle 7
0x00e: halt
bubble
bubble
Cycle 8
0x00c: addl %edx,%eax
0x00e: halt
Write Back
Memory
Execute
Decode
Fetch

## Slide 44: Pipeline Register Modes
Rising
clock
Rising
clock
_
_
Output = y
y
y
Rising
clock
Rising
clock
_
_
Output = x
x
x
x
x
n
o
p
Rising
clock
Rising
clock
_
_
Output =
nop
Output = x
Input = y
stall
= 0
bubble
= 0
x
x
Normal
Output = x
Input = y
stall
= 1
bubble
= 0
x
x
Stall
Output = x
Input = y
stall
= 0
bubble
= 1
Bubble

## Slide 45: Implementing Stalling
Pipeline Control
  Combinational logic detects stall condition
  Sets mode signals for how pipeline registers should update
E
M
W
F
D
CC
rB
srcA
srcB
icode
valE
valM
dstE
dstM
Cnd
icode
valE
valA
dstE
dstM
icode
ifun
valC
valA
valB
dstE
dstM
srcA
srcB
valC
valP
icode
ifun
rA
predPC
d_srcB
d_srcA
e_Cnd
D_icode
E_icode
M_icode
E_dstM
Pipe
control
logic
D_bubble
D_stall
E_bubble
F_stall
M_bubble
W_stall
set_cc
stat
stat
stat
stat
W_stat
stat
m_stat

## Slide 46: Data Forwarding
Naïve Pipeline
  Register isn’t written until completion of write-back stage
  Source operands read from register file in decode stage
    Needs to be in register file at start of stage
Observation
  Value generated in execute or memory stage
Trick
  Pass value directly from generating instruction to decode stage
  Needs to be available at end of decode stage

## Slide 47: Data Forwarding Example
  irmovl in write-back stage
  Destination value in W pipeline register
  Forward as valB for decode stage
0x000:
irmovl
$10,%
edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x006:
irmovl
$3,%
eax
F
D
E
M
W
F
D
E
M
W
0x00c:
nop
F
D
E
M
W
F
D
E
M
W
0x00d:
nop
F
D
E
M
W
F
D
E
M
W
0x00e:
addl
%
edx
,%
eax
F
D
E
M
W
F
D
E
M
W
0x010: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-h2.ys
Cycle 6
W
R[
%
eax
]
f
3
D
valA
f
R[
%
edx
]
=
10
valB
f
W_
valE
=
3
•
•
•
W_
dstE
=
%
eax
W_
valE
= 3
srcA
=
%
edx
srcB
=
%
eax

## Slide 48: Bypass Paths
Decode Stage
  Forwarding logic selects valA and valB
  Normally from register file
  Forwarding: get valA or valB from later pipeline stage
Forwarding Sources
  Execute: valE
  Memory: valE, valM
  Write back: valE, valM

## Slide 49: Data Forwarding Example #2
Register %edx
  Generated by ALU during previous cycle
  Forward from memory as valA
Register %eax
  Value just generated by ALU
  Forward from execute as valB

## Slide 50: Forwarding Priority
Multiple Forwarding Choices
  Which one should have priority
  Match serial semantics
  Use matching value from earliest pipeline stage
0x000: irmovl $1, %eax
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x006: irmovl $2, %eax
F
D
E
M
W
F
D
E
M
W
0x00c: irmovl $3, %eax
F
D
E
M
W
F
D
E
M
W
0x012: rrmovl %eax, %edx
F
D
E
M
W
F
D
E
M
W
0x014: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-priority.ys
W
R[
%
eax
]
f
3
W
R[
%
eax
]
f
1
D
valA
f
R[
%
edx
]
=
10
valB
f
R[
%
eax
]
=
0
D
valA
f
R[
%
edx
]
=
10
valB
f
R[
D
valA
f
R[
%
eax
]
=
?
valB
f
0
Cycle 5
W
R[
%
eax
]
f
3
M
R[
%
eax
]
f
2
W
R[
%
eax
]
f
3
E
R[
%
eax
]
f
3

## Slide 51: Implementing Forwarding
  Add additional feedback paths from E, M, and W pipeline registers into decode stage
  Create logic blocks to select from multiple sources for valA and valB in decode stage

## Slide 52: Implementing Forwarding
## What should be the A value?
int new_E_valA = [
# Use incremented PC
D_icode in { ICALL, IJXX } : D_valP;
# Forward valE from execute
d_srcA == e_dstE : e_valE;
# Forward valM from memory
d_srcA == M_dstM : m_valM;
# Forward valE from memory
d_srcA == M_dstE : M_valE;
# Forward valM from write back d_srcA == W_dstM : W_valM;
# Forward valE from write back
d_srcA == W_dstE : W_valE;
# Use value read from register file
1 : d_rvalA;
];

## Slide 53: Limitation of Forwarding
Load-use dependency
  Value needed by end of decode stage in cycle 7
  Value read from memory in memory stage of cycle 8

## Slide 54: Avoiding Load/Use Hazard
  Stall using instruction for one cycle
  Can then pick up loaded value by forwarding from memory stage

## Slide 55: Detecting Load/Use Hazard
Condition | Trigger
Load/Use Hazard | E_icode in { IMRMOVL, IPOPL } && E_dstM in { d_srcA, d_srcB }

## Slide 56: Control for Load/Use Hazard
  Stall instructions in fetch and decode stages
  Inject bubble into execute stage
0x000:
irmovl
$128,%
edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x006:
irmovl
$3,%
ecx
F
D
E
M
W
F
D
E
M
W
0x00c:
rmmovl
%
ecx
, 0(%
edx
)
F
D
E
M
W
F
D
E
M
W
0x012:
irmovl
$10,%
ebx
F
D
E
M
W
F
D
E
M
W
0x018:
mrmovl
0(%
edx
),
%
eax
# Load %
eax
F
D
E
M
W
F
D
E
M
W
# demo
-
luh
.
ys
0x01e:
addl
%
ebx
,
%
eax
# Use %
eax
0x020: halt
F
D
E
M
W
E
M
W
10
D
D
E
M
W
11
bubble
F
D
E
M
W
F
F
12
Condition | F | D | E | M | W
Load/Use Hazard | stall | stall | bubble | normal | normal

## Slide 57: Dealing with Dependencies between Instructions
Control Hazards

## Slide 58: Branch Misprediction Example
  Should only execute first 8 instructions
0x000: xorl %eax,%eax
0x002: jne t # Not taken
0x007: irmovl $1, %eax # Fall through
0x00d: nop
0x00e: nop
0x00f: nop
0x010: halt
0x011: t: irmovl $3, %edx # Target (Should not execute)
0x017: irmovl $4, %ecx # Should not execute
0x01d: irmovl $5, %edx # Should not execute
demo-j.ys

## Slide 59: Branch Misprediction Trace
  Incorrectly execute two instructions at branch target
0x000:
xorl
%
eax
,%
eax
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x002:
jne
t # Not taken
F
D
E
M
W
0x011: t:
irmovl
$3, %
edx
# Target
F
D
E
M
W
0x017:
irmovl
$4, %
ecx
# Target+1
F
D
E
M
W
0x007:
irmovl
$1, %
eax
# Fall Through
F
D
E
M
W
# demo
-
j
F
D
E
M
W
Cycle 5
E
valE
f
3
dstE
=
%
edx
E
valE
f
3
dstE
=
%
edx
M
M_Cnd =
0
M_
valA
= 0x007
D
valC
=
4
dstE
=
%
ecx
D
valC
=
4
dstE
=
%
ecx
F
valC
f
1
rB
f
%
eax
F
valC
f
1
rB
f
%
eax

## Slide 60: Handling Misprediction
Predict branch as taken
  Fetch 2 instructions at target
Cancel when mispredicted
  Detect branch not-taken in execute stage
  On following cycle, replace instructions in execute and decode by bubbles
  No side effects have occurred yet

## Slide 61: Detecting Mispredicted Branch
Condition | Trigger
Mispredicted Branch | E_icode = IJXX & !e_Cnd

## Slide 62: Control for Misprediction
Condition | F | D | E | M | W
Mispredicted Branch | normal | bubble | bubble | normal | normal

## Slide 63: Return Example
0x000: irmovl Stack,%esp # Initialize stack pointer
0x006: call p # Procedure call
0x00b: irmovl $5,%esi # Return point
0x011: halt
0x020: .pos 0x20
0x020: p: irmovl $-1,%edi # procedure
0x026: ret
0x027: irmovl $1,%eax # Should not be executed
0x02d: irmovl $2,%ecx # Should not be executed
0x033: irmovl $3,%edx # Should not be executed
0x039: irmovl $4,%ebx # Should not be executed
0x100: .pos 0x100
0x100: Stack: # Stack: Stack pointer
  Previously executed three additional instructions
demo-retb.ys

## Slide 64: Incorrect Return Example
  Incorrectly execute 3 instructions following ret

## Slide 65: Correct Return Example
0x026: ret
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
0x00b:
irmovl
$5,%
esi
# Return
F
D
E
M
W
# demo
-
retb
F
D
E
M
W
F
valC
f
5
rB
f
%
esi
F
valC
f
5
rB
f
%
esi
W
valM
=
0x0b
W
valM
=
0x0b
•
•
•
  As ret passes through pipeline, stall at fetch stage
    While in decode, execute, and memory stage
  Inject bubble into decode stage
  Release stall when reach write-back stage

## Slide 66: Detecting Return
Condition | Trigger
Processing ret | IRET in { D_icode, E_icode, M_icode }

## Slide 67: Control for Return
0x026: ret
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
0x00b:
irmovl
$5,%
esi
# Return
F
D
E
M
W
# demo
-
retb
F
D
E
M
W
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal

## Slide 68: Special Control Cases
Detection
Action (on next cycle)
Condition | Trigger
Processing ret | IRET in { D_icode, E_icode, M_icode }
Load/Use Hazard | E_icode in { IMRMOVL, IPOPL } && E_dstM in { d_srcA, d_srcB }
Mispredicted Branch | E_icode = IJXX & !e_Cnd
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Mispredicted Branch | normal | bubble | bubble | normal | normal

## Slide 69: Implementing Pipeline Control
  Combinational logic generates pipeline control signals
  Action occurs at start of following cycle
E
M
W
F
D
CC
rB
srcA
srcB
icode
valE
valM
dstE
dstM
Cnd
icode
valE
valA
dstE
dstM
icode
ifun
valC
valA
valB
dstE
dstM
srcA
srcB
valC
valP
icode
ifun
rA
predPC
d_srcB
d_srcA
e_Cnd
D_icode
E_icode
M_icode
E_dstM
Pipe
control
logic
D_bubble
D_stall
E_bubble
F_stall
M_bubble
W_stall
set_cc
stat
stat
stat
stat
W_stat
stat
m_stat

## Slide 70: Initial Version of Pipeline Control
bool F_stall =
# Conditions for a load/use hazard
E_icode in { IMRMOVL, IPOPL } && E_dstM in { d_srcA, d_srcB } ||
# Stalling at fetch while ret passes through pipeline
IRET in { D_icode, E_icode, M_icode };
bool D_stall =
# Conditions for a load/use hazard
E_icode in { IMRMOVL, IPOPL } && E_dstM in { d_srcA, d_srcB };
bool D_bubble =
# Mispredicted branch
(E_icode == IJXX && !e_Cnd) ||
# Stalling at fetch while ret passes through pipeline
IRET in { D_icode, E_icode, M_icode };
bool E_bubble =
# Mispredicted branch
(E_icode == IJXX && !e_Cnd) ||
# Load/use hazard
E_icode in { IMRMOVL, IPOPL } && E_dstM in { d_srcA, d_srcB };

## Slide 71: Control Combinations
  Special cases that can arise on same clock cycle
Combination A
  Not-taken branch
  ret instruction at branch target
Combination B
  Instruction that reads from memory to %esp
  Followed by ret instruction

## Slide 72: Control Combination A
  Should handle as mispredicted branch
  Stalls F pipeline register
  But PC selection logic will be using M_valM anyhow
JXX
E
D
M
Mispredict
JXX
E
D
M
Mispredict
E
ret
D
M
ret
1
E
ret
D
M
ret
1
E
ret
D
M
ret
1
Combination A
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Mispredicted Branch | normal | bubble | bubble | normal | normal
Combination | stall | bubble | bubble | normal | normal

## Slide 73: Control Combination B
  Would attempt to bubble and stall pipeline register D
  Signaled by processor as pipeline error
Load
E
Use
D
M
Load/use
E
ret
D
M
ret
1
E
ret
D
M
ret
1
E
ret
D
M
ret
1
Combination B
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | bubble + stall | bubble | normal | normal

## Slide 74: Handling Control Combination B
  Load/use hazard should get priority
  ret instruction should be held in decode stage for additional cycle
Load
E
Use
D
M
Load/use
E
ret
D
M
ret
1
E
ret
D
M
ret
1
E
ret
D
M
ret
1
Combination B
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | stall | bubble | normal | normal

## Slide 75: Corrected Pipeline Control Logic
  Load/use hazard should get priority
  ret instruction should be held in decode stage for additional cycle
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | stall | bubble | normal | normal
bool D_bubble =
# Mispredicted branch
(E_icode == IJXX && !e_Cnd) ||
# Stalling at fetch while ret passes through pipeline
IRET in { D_icode, E_icode, M_icode }
# but not condition for a load/use hazard
&& !(E_icode in { IMRMOVL, IPOPL }
&& E_dstM in { d_srcA, d_srcB });

## Slide 76: Pipeline Control Logic
  A sequence of control instructions complicates the control logic
    in particular, should stall in Decode stage (instead of bubble, as an initial inspection suggests)
  Load/use hazard should get priority
  ret instruction should be held in decode stage for additional cycle
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | stall | bubble | normal | normal

## Slide 77: Pipeline Summary
Concept
  Break instruction execution into 5 stages
  Run instructions through in pipelined mode
Limitations
  Can’t handle dependencies between instructions when instructions follow too closely
  Data dependencies
    One instruction writes register, later one reads it
  Control dependency
    Instruction sets PC in way that pipeline did not predict correctly
    Mispredicted branch and return

## Slide 78: Pipeline Summary
Data Hazards
  Most handled by forwarding
    No performance penalty
  Load/use hazard requires one cycle stall
Control Hazards
  Cancel instructions when detect mispredicted branch
    Two clock cycles wasted
  Stall fetch stage while ret passes through pipeline
    Three clock cycles wasted
Control Combinations
  Must analyze carefully
  First version had subtle bug
    Only arises with unusual instruction combination