## Slide 1: Arithmetic and Bitwise Operations on Binary Data CSCI 224 / ECE 317: Computer Architecture
Instructor:
Prof. Jason Fritts
Slides adapted from Bryant & O’Hallaron’s slides

## Slide 2: Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
And
A&B = 1 when both A=1 and B=1
Or
A|B = 1 when either A=1 or B=1
Not
~A = 1 when A=0
Exclusive-Or (Xor)
A^B = 1 when either A=1 or B=1, but not both

## Slide 3: Application of Boolean Algebra
Applied to Digital Systems by Claude Shannon
  1937 MIT Master’s Thesis
  Reason about networks of relay switches
    Encode closed switch as 1, open switch as 0
A
~A
~B
B
Connection when
A&~B | ~A&B
A&~B
~A&B
= A^B

## Slide 4: General Boolean Algebras
Operate on Bit Vectors
  Operations applied bitwise
  Bitwise-AND operator: &
  Bitwise-NOR operator: |
  Bitwise-XOR operator: ^
  Bitwise-NOT operator: ~
All of the Properties of Boolean Algebra Apply
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01000001
01111101
00111100
10101010

## Slide 5: Representing & Manipulating Sets
Representation
  Width w bit vector represents subsets of {0, …, w–1}
  aj = 1 if j ∈ A
    01101001 { 0, 3, 5, 6 }
    76543210
    01010101 { 0, 2, 4, 6 }
    76543210
Operations
  & Intersection 01000001 { 0, 6 }
  | Union 01111101 { 0, 2, 3, 4, 5, 6 }
  ^ Symmetric difference 00111100 { 2, 3, 4, 5 }
  ~ Complement 10101010 { 1, 3, 5, 7 }

## Slide 6: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (char data type):
  in hexadecimal in binary
  ~0x41 ➙ 0xBE // ~010000012 ➙ 101111102
  ~0x00 ➙ 0xFF // ~000000002 ➙ 111111112
  0x69 & 0x55 ➙ 0x41 // 011010012 & 010101012 ➙ 010000012
  0x69 | 0x55 ➙ 0x7D // 011010012 | 010101012 ➙ 011111012

## Slide 7: Contrast: Logic Operations in C
Contrast to Logical Operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type):
  !0x41 ➙ 0x00
  !0x00 ➙ 0x01
  !!0x41 ➙ 0x01
  0x69 && 0x55 ➙ 0x01
  0x69 || 0x55 ➙ 0x01
  p && *p // avoids null pointer access

## Slide 8: Shift Operations
Left Shift: x << y
  Shift bit-vector x left y positions
      Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on right
Undefined Behavior
  Shift amount < 0 or ≥ word size
01100010
Argument x
00010000
<< 3
00011000
Log. >> 2
00011000
Arith. >> 2
10100010
Argument x
00010000
<< 3
00101000
Log. >> 2
11101000
Arith. >> 2
00010000
00010000
00011000
00011000
00011000
00011000
00010000
00101000
11101000
00010000
00101000
11101000

## Slide 9: Bitwise-NOT: One’s Complement
Bitwise-NOT operation: ~
  Bitwise-NOT of x is ~x
  Flip all bits of x to compute ~x
    flip each 1 to 0
    flip each 0 to 1
Complement
  Given x == 10011101
  Flip bits (one’s complement):
1
0
0
1
0
1
1
1
x:
0
1
1
0
1
0
0
0
~x:

## Slide 10: Negation: Two’s Complement
Negate a number by taking 2’s Complement
  Flip bits (one’s complement) and add 1
  ~x + 1 == -x
Negation (Two’s Complement):
  Given x == 10011101
  Flip bits (one’s complement):
  Add 1:
1
0
0
1
0
1
1
1
x:
0
1
1
0
1
0
0
0
~x:
+
1
0
1
1
0
1
1
0
0
-x:

## Slide 11: Complement & Increment Examples
x = 15213
x = 0

## Slide 12: Unsigned Addition
Addition Operation
  Carry output dropped at end of addition
  Valid ONLY if true sum is within w-bit range
Example #1:
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
0
1
1
0
1
0
0
0
9810
+
1
0
1
1
0
0
0
1
17210
0
1
0
0
1
0
0
1
7410
1
0
1
Valid in 8-bit
unsigned range

## Slide 13: Unsigned Addition
Example #2:
0
1
1
1
1
0
0
1
11010
+
0
0
1
0
0
0
1
1
5610
1
1
0
0
1
0
0
1
20210
1
1
1
Not Valid in 8-bit
unsigned range
(312 is > 255)
0
1
1
0
1
0
0
0
1008210
+
1
0
1
1
0
0
0
1
452410
0
1
0
0
1
0
0
1
5997810
1
1
1
1
1
1
Example #3:
0
0
1
1
1
1
0
0
1
1
1
0
1
0
0
1
0
0
0
0
0
1
1
0
1
1
1
1
1
1
Not Valid in 16-bit
unsigned range
(70060 is > 65535)

## Slide 14: Visualizing (Mathematical) Integer Addition
Integer Addition
  4-bit integers u, v
  Compute true sum
  Values increase linearly with u and v
  Forms planar surface
u
v

## Slide 15: Visualizing Unsigned Addition
Wraps Around
  If true sum ≥ 2w
  At most once
0
2w
2w+1
u
v
True Sum
Modular Sum
Overflow
Overflow

## Slide 16: Visualizing Signed Addition
Values
  4-bit two’s comp.
  Range from -8 to +7
Wraps Around
  If sum  2w–1
    Becomes negative
    At most once
  If sum < –2w–1
    Becomes positive
    At most once
u
v
PosOver
NegOver

## Slide 17: Signed Addition
Example #1:
0
1
1
1
1
0
0
1
11010
+
0
0
1
0
0
0
1
1
5610
1
1
0
0
1
0
0
1
-5410
1
1
1
Valid in 8-bit
signed range
(-128 < 56 < 127)
1
1
1
Example #2:
0
1
1
0
1
0
0
0
9810
+
1
0
1
1
0
0
0
1
-8410
0
1
0
0
1
0
0
1
7410
1
0
1
Note: Same bytes as for Ex #1 and Ex #2
in unsigned integer addition, but
now interpreted as 8-bit signed integers
Not Valid in 8-bit
signed range
(172 > 127)

## Slide 18: Arithmetic: Basic Rules
Unsigned ints, 2’s complement ints are isomorphic rings: isomorphism = casting
Left shift
  Unsigned/signed: multiplication by 2k
  Always logical shift
Right shift
  Unsigned: logical shift, div (division + round to zero) by 2k
  Signed: arithmetic shift
    Positive numbers: div (division + round to zero) by 2k
    Negative numbers: div (division + round away from zero) by 2k Use biasing to fix

## Slide 19: Integer C Puzzles
x < 0  ((x*2) < 0)
ux >= 0
x & 7 == 7  (x<<30) < 0
ux > -1
x > y  -x < -y
x * x >= 0
x > 0 && y > 0  x + y > 0
x >= 0  -x <= 0
x <= 0  -x >= 0
(x|-x)>>31 == -1
ux >> 3 == ux/8
x >> 3 == x/8
x & (x-1) != 0
int x = foo();
int y = bar();
unsigned ux = x;
unsigned uy = y;
Initialization