## Slide 1: Machine-Level Programming I – Introduction CSCI 224 / ECE 317: Computer Architecture
Instructor:
Prof. Jason Fritts
Slides adapted from Bryant & O’Hallaron’s slides

## Slide 2: Machine Programming I – Basics
Instruction Set Architecture
  Software Architecture vs. Hardware Architecture
  Common Architecture Classifications
The Intel x86 ISA – History and Microarchitectures
Dive into C, Assembly, and Machine code
The Intel x86 Assembly Basics:
  Registers and Operands
  mov instruction
Intro to x86-64
    AMD was first!

## Slide 3: Hardware vs. Software Architecture
There are two parts to the computer architecture of a processor:
  Software architecture
    commonly know as the Architecture or Instruction Set Architecture (ISA)
  Hardware architecture
    commonly know as the Microarchitecture
The (software) architecture includes all aspects of the design that are visible to programmers
The microarchitecture refers to one specific implementation of a software architecture
  e.g. number of cores, processor frequency, cache sizes, instructions supported, etc.
  the set of all independent hardware architectures for a given software architecture is known as the processor family
    e.g. the Intel x86 family

## Slide 4: Assembly Programmer’s View
CPU
Programmer-Visible State
  PC: Program counter
    Holds address of next instruction
  Register file
    Temp storage for program data
  Condition codes
    Store status info about recent operation
    Used for conditional branching
PC
Registers
Memory
Object Code
Program Data
OS Data
Addresses
Data
Instructions
Stack
Condition
Codes
  Memory
    Byte addressable array
    Code, user data, (some) OS data
    Includes stack used to support procedures

## Slide 5: Separation of hardware and software
The reason for the separation of the (software) architecture from the microarchitecture (hardware) is backwards compatibility
Backwards compatibility ensures:
  software written on older processors will run on newer processors (of the same ISA)
  processor families can always utilize the latest technology by creating new hardware architectures (for the same ISA)
However, new microarchitectures often add to the (software) architecture, so software written on newer processors may not run on older processors

## Slide 6: Parts of the Software Architecture
There are 4 parts to the (software) architecture
  instruction set
    the set of available instructions and the rules for using them
  register file organization
    the number, size, and rules for using registers
  memory organization & addressing
    the organization of the memory and the rules for accessing data
  operating modes
    the various modes of execution for the processor
    there are usually at least two modes:
      user mode (for general use)
      system mode (allows access to privileged instructions and memory)

## Slide 7: Software Architecture: Instruction Set
The Instruction Set defines
  the set of available instructions
  fundamental nature of the instructions
    simple and fast
    complex and concise
  instruction formats
    define the rules for using the instructions
  the width (in bits) of the datapath
    this defines the fundamental size of data in the CPU, including:
      the size (number of bits) for the data buses in the CPU
      the number of bits per register in the register file
      the width of the processing units
      the number of address bits for accessing memory

## Slide 8: Software Architecture: Instruction Set
There are 9 fundamental categories of instructions
  arithmetic
    these instruction perform integer arithmetic, such as add, subtract, multiply, and negate
      Note: integer division is commonly done in software
  logical
    these instructions perform Boolean logic (AND, OR, NOT, etc.)
  relational
    these instructions perform comparisons, including ==, !=, <, >, <=, >=
    some ISAs perform comparisons in the conditional branches
  control
    these instructions enable changes in control flow, both for decision making and modularity
    the set of control instruction includes:
      conditional branches
      unconditional jumps
      procedure calls and returns

## Slide 9: Software Architecture: Instruction Set
  memory
    these instructions allow data to be read from or written to memory
  floating-point
    these instruction perform real-number operations, including add, subtract, multiply, division, comparisons, and conversions
  shifts
    these instructions allow bits to be shifted or rotated left or right
  bit manipulation
    these instructions allow data bits to be set or cleared
    some ISAs do not provide these, since they can be done via logic instructions
  system instructions
    specialized instructions for system control purposes, such as
      STOP or HALT (stop execution)
      cache hints
      interrupt handling
    some of these instructions are privileged, requiring system mode

## Slide 10: Software Architecture: Register File
The Register File is a small, fast temporary storage area in the processor’s CPU
  it serves as the primary place for holding data values currently being operated upon by the CPU
The organization of the register file determines
  the number of registers
    a large number of registers is desirable, but having too many will negatively impact processor speed
  the number of bits per register
    this is equivalent to the width of the datapath
  the purpose of each register
    ideally, most registers should be general-purpose
    however, some registers serve specific purposes

## Slide 11: Purpose of Register File
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compilers store values in registers whenever possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 12: Software Architecture: Memory
The Memory Organization & Addressing defines
  how memory is organized in the architecture
    where data and program memory are unified or separate
    the amount of addressable memory
      usually determined by the datapath width
    the number of bytes per address
      most processors are byte-addressable, so each byte has a unique addr
    whether it employs virtual memory, or just physical memory
      virtual memory is usually required in complex computer systems, like desktops, laptops, servers, tablets, smart phones, etc.
      simpler systems use embedded processors with only physical memory
  rules identifying how instructions access data in memory
    what instructions may access memory (usually only loads, stores)
    what addressing modes are supported
    the ordering and alignment rules for multi-byte primitive data types

## Slide 13: Software Architecture: Operating Modes
Operating Modes define the processor’s modes of execution
The ISA typically supports at least two operating modes
  user mode
    this is the mode of execution for typical use
  system mode
    allows access to privileged instructions and memory
    aside from interrupt and exception handling, system mode is typically only available to system programmers and administrators
Processors also generally have hardware testing modes, but these are usually part of the microarchitecture, not the (software) architecture

## Slide 14: Machine Programming I – Basics
Instruction Set Architecture
  Software Architecture vs. Hardware Architecture
  Common Architecture Classifications
The Intel x86 ISA – History and Microarchitectures
Dive into C, Assembly, and Machine code
The Intel x86 Assembly Basics:
  Registers
  Operands
  mov instruction
Intro to x86-64
    AMD was first!

## Slide 15: Common Architecture (ISA) Classifications:
Concise vs. Fast: CISC vs. RISC
  CISC – Complex Instruction Set Computers
    complex instructions targeting efficient program representation
    variable-length instructions
    versatile addressing modes
    specialized instructions and registers implement complex tasks
    NOT optimized for speed – tend to be SLOW
  RISC – Reduced Instruction Set Computers
    small set of simple instructions targeting high speed implementation
    fixed-length instructions
    simple addressing modes
    many general-purpose registers
    leads to FAST hardware implementations
    but less memory efficient

## Slide 16: Classifications: Unified vs. Separate Memory
von Neumann vs. Harvard architecture
  relates to whether program and data in unified or separate memory
  von Neumann architecture
    program and data are stored in the same unified memory space
    requires only one physical memory
    allows self-modifying code
    however, code and data must share the same memory bus
    used by most general-purpose processors (e.g. Intel x86)
  Harvard architecture
    program and data are stored in separate memory spaces
    requires separate physical memory
    code and data do not share same bus, giving higher bandwidths
    often used by digital signal processors for data-intensive applications

## Slide 17: Classifications: Performance vs. Specificity
Microprocessor vs. Microcontroller
  Microprocessor
    processors designed for high-performance and flexibility in personal computers and other general purpose applications
    architectures target high performance through a combination of high speed and parallelism
    processor chip contains only CPU(s) and cache
    no peripherals included on-chip
  Microcontroller
    processors designed for specific purposes in embedded systems
    only need performance sufficient to needs of that application
    processor chip generally includes:
      a simple CPU
      modest amounts of RAM and (Flash) ROM
      appropriate peripherals needed for specific application
    also often need to meet low power and/or real-time requirements

## Slide 18: Machine Programming I – Basics
Instruction Set Architecture
  Software Architecture vs. Hardware Architecture
  Common Architecture Classifications
The Intel x86 ISA – History and Microarchitectures
Dive into C, Assembly, and Machine code
The Intel x86 Assembly Basics:
  Registers
  Operands
  mov instruction
Intro to x86-64
    AMD was first!

## Slide 19: Intel x86 Processors
The main software architecture for Intel is the x86 ISA
  also known as IA-32
  for 64-bit processors, it is known as x86-64
Totally dominate laptop/desktop/server market
Evolutionary design
  Backwards compatible back to 8086, introduced in 1978
  Added more features as time goes on
Complex instruction set computer (CISC)
  Many different instructions with many different formats
    but, only small subset used in Linux programs

## Slide 20: Intel x86 Family: Many Microarchitectures
X86-64 / Intel 64
X86-32 / IA32
X86-16
8086
286
386
486
Pentium
Pentium MMX
Pentium III
Pentium 4
Pentium 4E
Pentium 4F
Core 2 Duo
Core i7
IA: often redefined as latest Intel architecture
time
Architectures
Processors
MMX
SSE
SSE2
SSE3
SSE4

## Slide 21: Software architecture can grow
Backward compatibility does not mean instruction set is fixed
  new instructions and functionality can be added to the software architecture over time
Intel added additional features over time
  Instructions to support multimedia operations (MMX, SSE)
    SIMD parallelism – same operation done across multiple data
  Instructions enabling more efficient conditional operations
x86 instruction set

## Slide 22: Intel x86: Milestones & Trends
Name Date Transistors MHz
8086 1978 29K 5-10
  First 16-bit processor. Basis for IBM PC & DOS
  1MB address space
386 1985 275K 16-33
  First 32 bit processor, referred to as IA32
  Added “flat addressing”
Pentium 1993 3.1M 50-75
Pentium II 1996 7.5M 233-300
Pentium III 1999 9.5-21M 450-800
Pentium 4F 2004 169M 3200-3800
  First 64-bit processor
  Got very hot
Core i7 2008 731M 2667-3333

## Slide 23: But IA-32 is CISC? How does it get speed?
  Hard to match RISC performance, but Intel has done just that! ….In terms of speed; less so for power
CISC instruction set makes implementation difficult
  Hardware translates instructions to simpler micro-operations
    simple instructions: 1–to–1
    complex instructions: 1–to–many
  Micro-engine similar to RISC
  Market share makes this economically viable
Comparable performance to RISC
  Compilers avoid CISC instructions

## Slide 24: Processor Trends
Number of transistors has continued to double every 2 years
In 2004 – we hit the Power Wall
  Processor clock speeds started to leveled off

## Slide 25: Machine Programming I – Basics
Instruction Set Architecture
  Software Architecture (“Architecture” or “ISA”) vs.
  Hardware Architecture (“Microarchitecture”)
The Intel x86 ISA – History and Microarchitectures
Dive into C, Assembly, and Machine code
The Intel x86 Assembly Basics:
  Registers
  Operands
  mov instruction
Intro to x86-64
    AMD was first!

## Slide 26: Turning C into Object Code
text
text
binary
binary
Compiler (gcc –S –m32)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc –O1 –m32 p1.c p2.c -o p
    Use basic optimizations (-O1)
    Put resulting binary in file p
    On 64-bit machines, specify 32-bit x86 code (-m32)

## Slide 27: Compiling Into Assembly
C Code
int sum(int x, int y)
{
int t = x+y;
return t;
}
Generated IA32 Assembly
sum:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
addl 8(%ebp),%eax
popl %ebp
ret
Obtain with command:
  gcc –O1 -S –m32 code.c
-S specifies compile to assembly (vs object) code, and produces file code.s
Some compilers use instruction “leave”

## Slide 28: Assembly Characteristics: Simple Types
Integer data of 1, 2, or 4 bytes
  Data values
  Addresses (void* pointers)
Floating point data of 4, 8, or 10 bytes
No concept of aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory

## Slide 29: Assembly Characteristics: Operations
Perform some operation on register or memory data
  arithmetic
  logical
  bit shift or manipulation
  comparison (relational)
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Transfer control
  Unconditional jumps to/from procedures
  Conditional branches

## Slide 30: Object Code
Code for sum
0x401040 <sum>:
0x55
0x89
0xe5
0x8b
0x45
0x0c
0x03
0x45
0x08
0x5d
0xc3
Assembler
  Translates .s into .o
  Binary encoding of each instruction
  Nearly-complete image of executable code
  Missing linkages between code in different files
Linker
  Resolves references between files
  Combines with static run-time libraries
    E.g., code for malloc, printf
  Some libraries are dynamically linked
    Linking occurs when program begins execution
  Total of 11 bytes
  Each instruction 1, 2, or 3 bytes
  Starts at address 0x401040

## Slide 31: Machine Instruction Example
C Code
  Add two signed integers
Assembly
  Add 2 4-byte integers
    “Long” words in GCC parlance
    Same instruction whether signed or unsigned
  Operands:
    x: Register %eax
    y: Memory M[%ebp+8]
    t: Register %eax
      Return function value in %eax
Object Code
  3-byte instruction
  Stored at address 0x80483ca
int t = x+y;
addl 8(%ebp),%eax
0x80483ca: 03 45 08
Similar to expression:
x += y
More precisely:
int eax;
int *ebp;
eax += ebp[2]

## Slide 32: Disassembling Object Code
Disassembled
Disassembler
  objdump -d p
  Useful tool for examining object code
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can be run on either a.out (complete executable) or .o file
080483c4 <sum>:
80483c4: 55 push %ebp
80483c5: 89 e5 mov %esp,%ebp
80483c7: 8b 45 0c mov 0xc(%ebp),%eax
80483ca: 03 45 08 add 0x8(%ebp),%eax
80483cd: 5d pop %ebp
80483ce: c3 ret

## Slide 33: Alternate Disassembly
Disassembled
Dump of assembler code for function sum:
0x080483c4 <sum+0>: push %ebp
0x080483c5 <sum+1>: mov %esp,%ebp
0x080483c7 <sum+3>: mov 0xc(%ebp),%eax
0x080483ca <sum+6>: add 0x8(%ebp),%eax
0x080483cd <sum+9>: pop %ebp
0x080483ce <sum+10>: ret
Within gdb Debugger
  gdb p
  disassemble sum
  Disassemble procedure
  x/11xb sum
  Examine the 11 bytes starting at sum
Object
0x401040:
0x55
0x89
0xe5
0x8b
0x45
0x0c
0x03
0x45
0x08
0x5d
0xc3

## Slide 34: What Can be Disassembled?
Anything that can be interpreted as executable code
Disassembler examines bytes and reconstructs assembly source
% objdump -d WINWORD.EXE
WINWORD.EXE: file format pei-i386
No symbols in "WINWORD.EXE".
Disassembly of section .text:
30001000 <.text>:
30001000: 55 push %ebp
30001001: 8b ec mov %esp,%ebp
30001003: 6a ff push $0xffffffff
30001005: 68 90 10 00 30 push $0x30001090
3000100a: 68 91 dc 4c 30 push $0x304cdc91

## Slide 35: Machine Programming I – Basics
Instruction Set Architecture
  Software Architecture vs. Hardware Architecture
  Common Architecture Classifications
The Intel x86 ISA – History and Microarchitectures
Dive into C, Assembly, and Machine code
The Intel x86 Assembly Basics:
  Common instructions
  Registers, Operands, and mov instruction
  Addressing modes
Intro to x86-64
    AMD was first!

## Slide 36: Typical Instructions in Intel x86
Arithmetic
  add, sub, neg, imul, div, inc, dec, leal, …
Logical (bit-wise Boolean)
  and, or, xor, not
Relational
  cmp, test, sete, …
Control
  je, jle, jg, jb, jmp, call, ret, …
Moves & Memory Access
  mov, push, pop, movswl, movzbl, cmov, …
  nearly all x86 instructions can access memory
Shifts
  shr, sar, shl, sal (same as shl)
Floating-point
  fld, fadd, fsub, fxch, addsd, movss, cvt…, ucom…
  float-point change completely with x86-64

## Slide 37: CISC Instructions: Variable-Length

## Slide 38: Machine Programming I – Basics
Instruction Set Architecture
  Software Architecture (“Architecture” or “ISA”) vs.
  Hardware Architecture (“Microarchitecture”)
The Intel x86 ISA – History and Microarchitectures
Dive into C, Assembly, and Machine code
The Intel x86 Assembly Basics:
  Common instructions
  Registers, Operands, and mov instruction
  Addressing modes
Intro to x86-64
    AMD was first!

## Slide 39: Integer Registers (IA32)
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
%ax
%cx
%dx
%bx
%si
%di
%sp
%bp
%ah
%ch
%dh
%bh
%al
%cl
%dl
%bl
16-bit virtual registers
(backwards compatibility)
general purpose
accumulate
counter
data
base
source
index
destination
index
stack
pointer
base
pointer
Origin
(mostly obsolete)

## Slide 40: Moving Data: IA32
Moving Data
  movl Source, Dest
Operand Types
  Immediate: Constant integer data
    example: $0x400, $-533
    like C constant, but prefixed with ‘$’
    encoded with 1, 2, or 4 bytes
  Register: One of 8 integer registers
    example: %eax, %edx
    but %esp and %ebp reserved for special use
    others have special uses in particular situations
  Memory: 4 consecutive bytes of memory at address given by register
    simplest example: (%eax)
    various other “address modes”
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp

## Slide 41: movl Operand Combinations
Cannot do memory-memory transfer with a single instruction
movl
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movl $0x4,%eax
temp = 0x4;
movl $-147,(%eax)
*p = -147;
movl %eax,%edx
temp2 = temp1;
movl %eax,(%edx)
*p = temp;
movl (%eax),%edx
temp = *p;
Src, Dest

## Slide 42: Machine Programming I – Basics
Instruction Set Architecture
  Software Architecture (“Architecture” or “ISA”) vs.
  Hardware Architecture (“Microarchitecture”)
The Intel x86 ISA – History and Microarchitectures
Dive into C, Assembly, and Machine code
The Intel x86 Assembly Basics:
  Common instructions
  Registers, Operands, and mov instruction
  Addressing modes
Intro to x86-64
    AMD was first!

## Slide 43: Simple Memory Addressing Modes
Normal: (R) Mem[Reg[R]]
  Register R specifies memory address movl (%ecx),%eax
Displacement: D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movl 8(%ebp),%edx

## Slide 44: Using Simple Addressing Modes
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
Body
Set
Up
Finish
swap:
pushl %ebx
movl 8(%esp), %edx
movl 12(%esp), %eax
movl (%edx), %ecx
movl (%eax), %ebx
movl %ebx, (%edx)
movl %ecx, (%eax)
popl %ebx
ret

## Slide 45: Using Simple Addressing Modes
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
pushl %ebx
movl 8(%esp), %edx
movl 12(%esp), %eax
movl (%edx), %ecx
movl (%eax), %ebx
movl %ebx, (%edx)
movl %ecx, (%eax)
popl %ebx
ret
Body
Set
Up
Finish

## Slide 46: Understanding Swap
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
Stack
(in memory)
Register Value
%edx xp
%ecx yp
%ebx t0
%eax t1
yp
xp
Rtn adr
Old %ebx
%esp
0
4
8
12
Offset
•
•
•
movl 8(%esp), %edx # edx = xp
movl 12(%esp), %eax # eax = yp
movl (%edx), %ecx # ecx = *xp (t0)
movl (%eax), %ebx # ebx = *yp (t1)
movl %ebx, (%edx) # *xp = t1
movl %ecx, (%eax) # *yp = t0

## Slide 47: Understanding Swap
0x120
0x124
Rtn adr
%esp
0
4
8
12
Offset
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x104
movl 8(%esp), %edx # edx = xp
movl 12(%esp), %eax # eax = yp
movl (%edx), %ecx # ecx = *xp (t0)
movl (%eax), %ebx # ebx = *yp (t1)
movl %ebx, (%edx) # *xp = t1
movl %ecx, (%eax) # *yp = t0

## Slide 48: Understanding Swap
0x120
0x124
Rtn adr
%esp
0
4
8
12
Offset
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x124
0x104
movl 8(%esp), %edx # edx = xp
movl 12(%esp), %eax # eax = yp
movl (%edx), %ecx # ecx = *xp (t0)
movl (%eax), %ebx # ebx = *yp (t1)
movl %ebx, (%edx) # *xp = t1
movl %ecx, (%eax) # *yp = t0
0x124

## Slide 49: Understanding Swap
0x120
0x124
Rtn adr
%esp
0
4
8
12
Offset
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x120
0x104
0x124
movl 8(%esp), %edx # edx = xp
movl 12(%esp), %eax # eax = yp
movl (%edx), %ecx # ecx = *xp (t0)
movl (%eax), %ebx # ebx = *yp (t1)
movl %ebx, (%edx) # *xp = t1
movl %ecx, (%eax) # *yp = t0
0x120

## Slide 50: Understanding Swap
456
0x120
0x124
Rtn adr
%esp
0
4
8
12
Offset
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x124
123
0x104
0x120
movl 8(%esp), %edx # edx = xp
movl 12(%esp), %eax # eax = yp
movl (%edx), %ecx # ecx = *xp (t0)
movl (%eax), %ebx # ebx = *yp (t1)
movl %ebx, (%edx) # *xp = t1
movl %ecx, (%eax) # *yp = t0
123

## Slide 51: Understanding Swap
0x120
0x124
Rtn adr
%esp
0
4
8
12
Offset
123
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x120
0x124
123
0x104
456
movl 8(%esp), %edx # edx = xp
movl 12(%esp), %eax # eax = yp
movl (%edx), %ecx # ecx = *xp (t0)
movl (%eax), %ebx # ebx = *yp (t1)
movl %ebx, (%edx) # *xp = t1
movl %ecx, (%eax) # *yp = t0
456

## Slide 52: Understanding Swap
456
0x120
0x124
Rtn adr
%esp
0
4
8
12
Offset
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x104
0x120
0x124
123
456
movl 8(%esp), %edx # edx = xp
movl 12(%esp), %eax # eax = yp
movl (%edx), %ecx # ecx = *xp (t0)
movl (%eax), %ebx # ebx = *yp (t1)
movl %ebx, (%edx) # *xp = t1
movl %ecx, (%eax) # *yp = t0
456

## Slide 53: Understanding Swap
0x120
0x124
Rtn adr
%esp
0
4
8
12
Offset
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x104
0x120
0x124
123
456
movl 8(%esp), %edx # edx = xp
movl 12(%esp), %eax # eax = yp
movl (%edx), %ecx # ecx = *xp (t0)
movl (%eax), %ebx # ebx = *yp (t1)
movl %ebx, (%edx) # *xp = t1
movl %ecx, (%eax) # *yp = t0
123

## Slide 54: Complete Memory Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[ Reg[Rb] + S * Reg[Ri] + D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 8 integer registers
  Ri: Index register: Any, except for %esp (likely not %ebp either)
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases
(Rb,Ri) Mem[ Reg[Rb] + Reg[Ri] ]
D(Rb,Ri) Mem[ Reg[Rb] + Reg[Ri] + D]
(Rb,Ri,S) Mem[ Reg[Rb]+ S * Reg[Ri] ]

## Slide 55: Basic x86 Addressing Modes
Memory addressing modes
  Address in register
    Address = Rbase + displacement
    Address = Rbase + Rindex
    Address = Rbase + 2scale × Rindex (scale = 0, 1, 2, or 3)
    Address = Rbase + 2scale × Rindex + displacement

## Slide 56: Machine Programming I – Basics
Instruction Set Architecture
  Software Architecture vs. Hardware Architecture
  Common Architecture Classifications
The Intel x86 ISA – History and Microarchitectures
Dive into C, Assembly, and Machine code
The Intel x86 Assembly Basics:
  Common instructions
  Registers, Operands, and mov instruction
  Addressing modes
Intro to x86-64
    AMD was first!

## Slide 57: AMD created first 64-bit version of x86
Historically
  AMD has followed just behind Intel
  A little bit slower, a lot cheaper
2003, developed 64-bit version of x86: x86-64
  Recruited top circuit designers from DEC and other diminishing companies
  Built Opteron: tough competitor to Pentium 4

## Slide 58: Intel’s 64-Bit
Intel Attempted Radical Shift from IA32 to IA64
  Totally different architecture (Itanium)
  Executes IA32 code only as legacy
  Performance disappointing
2003: AMD Stepped in with Evolutionary Solution
  Originally called x86-64 (now called AMD64)
2004: Intel Announces their 64-bit extension to IA32
  Originally called EMT64 (now called Intel 64)
  Almost identical to x86-64!
Collectively known as x86-64
  minor differences between the two

## Slide 59: Data Representations: IA32 vs. x86-64
Sizes of C Objects (in bytes)
  C Data Type Intel IA32 x86-64
    unsigned 4 4
    int 4 4
    long int 4 8
    char 1 1
    short 2 2
    float 4 4
    double 8 8
    long double 10/12 16
    pointer (e.g. char *) 4 8

## Slide 60: x86-64 Integer Registers
  Extend existing registers. Add 8 new ones.
  Make %ebp/%rbp general purpose
%rsp
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 61: New Instructions for 64-bit Operands
Long word l (4 Bytes) ↔ Quad word q (8 Bytes)
New instructions:
  movl ➙ movq
  addl ➙ addq
  sall ➙ salq
  etc.
32-bit instructions that generate 32-bit results
  Set higher order bits of destination register to 0
  Example: addl

## Slide 62: 32-bit code for int swap
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
Body
Set
Up
Finish
swap:
pushl %ebx
movl 8(%esp), %edx
movl 12(%esp), %eax
movl (%edx), %ecx
movl (%eax), %ebx
movl %ebx, (%edx)
movl %ecx, (%eax)
popl %ebx
ret

## Slide 63: 64-bit code for int swap
Operands passed in registers (why useful?)
  First input arg (xp) in %rdi, second input arg (yp) in %rsi
  64-bit pointers
No stack operations required
32-bit ints held temporarily in %eax and %edx
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
Body
Set
Up
Finish
swap:
movl (%rdi), %edx
movl (%rsi), %eax
movl %eax, (%rdi)
movl %edx, (%rsi)
ret

## Slide 64: 64-bit code for long int swap
64-bit long ints
  Pass input arguments in registers %rax and %rdx
  movq operation
    “q” stands for quad-word
void swap(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Body
Set
Up
Finish
swap_l:
movq (%rdi), %rdx
movq (%rsi), %rax
movq %rax, (%rdi)
movq %rdx, (%rsi)
ret

## Slide 65: Machine Programming I – Basics
Instruction Set Architecture
  Software Architecture vs. Hardware Architecture
  Common Architecture Classifications
The Intel x86 ISA – History and Microarchitectures
Dive into C, Assembly, and Machine code
The Intel x86 Assembly Basics:
  Common instructions
  Registers, Operands, and mov instruction
  Addressing modes
Intro to x86-64
    AMD was first!

## Slide 66: Machine Programming I – Summary
Instruction Set Architecture
  Many different varieties and features of processor architectures
  Separation of (software) Architecture and Microarchitecture is key for backwards compatibility
The Intel x86 ISA – History and Microarchitectures
  Evolutionary design leads to many quirks and artifacts
Dive into C, Assembly, and Machine code
  Compiler must transform statements, expressions, procedures into low-level instruction sequences
The Intel x86 Assembly Basics:
  The x86 move instructions cover wide range of data movement forms
Intro to x86-64
  A major departure from the style of code seen in IA32

## Slide 67: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs

## Slide 68: Basic x86 Registers